## Slide 1: CACHE OPTIMIZATION
COMPUTER ARCHITECTURE CE6304
Submitted by
Ayushi Chourasia – akc170630 (100%)
Yiheng Gao - yxg171130 (100%)
Project#2

## Slide 2: Objectives
Introduction
Project Definition
Calculate the CPI of given parameters.
Optimize CPI for each benchmarks.
Defining cost function.
Optimize caches for cost/performance

## Slide 3: Introduction
Cache is a smaller memory which can be accessed very quickly. It stores the data and applications that are frequently used by the processor. Hence Cache design choices affect the performance of a microprocessor.
During execution, the processor uses data from the cache to increase the speed of execution as the processor does not need to search for data in the main memory.
Thus, in this project the aim is to optimize various cache design choices by making sensible tradeoff between cost and performance of the CPU.

## Slide 4: PART 1
Project Definition

## Slide 5: Project Definition
In this project, we tuned the cache hierarchy on X86 architecture bases on the gem5 simulator. The cache design parameters are as follows:
CPU Types: Different CPU models.
Cache levels: No cache at all, one level or two levels.
Size: Cache size, one of the most important choices.
Associativity: Selection of cache associativity (e.g. direct mapped, 2-way set associative, etc.).
Block size: Block size of the cache, usually 64 or 32 bytes.
While larger caches generally mean better performance, they also come at a greater cost. Thus, sensible design choices and trade-offs are required.

## Slide 6: Project Definition
The gem5 simulator is a modular platform for computer-system architecture research, encompassing system-level architecture as well as processor microarchitecture. In this project Gem 5 is used to model the different cache choices for the provided benchmarks using different configurations

## Slide 7: PART 2
CPI for given configuration

## Slide 8: Given Configurations
CPU Models: TimingSimpleCPU (timing), DerivO3CPU (detailed), MinorCPU (minor).
Cache levels: Two levels.
Unified caches: Separate L1 data and L1 instruction caches, unified L2 cache.
Size: 128KB L1 data cache, 128KB L1 instruction cache, 1MB unified L2 cache.
Associativity: Two way for L1 caches, Direct Mapped for L2 cache.
Block size: 64 bytes.
Block replacement policy: Least Recent Used policy (LRU).

## Slide 9: CPI Formula
CPI is a measure of performance of the CPU as it is the number of clock cycles per instruction. A lower CPI indicates better performance.

## Slide 10: Configurations
PARAMETERS | VALUES
CPU TIMING | TIMING
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 2
BLOCK SIZE | 64kB
L1 DATA CACHE SIZE | 128kB
L1 DATA ASSOCIATIVITY | 2
L1 INSTRUCTION CACHE SIZE | 128kB
L1 INSTRUCTION ASSOCIATIVITY | 2

## Slide 11: CPI OF ALL THE BENCHMARKS
 | 401.bzip2 | 429.mcf | 456.hmmer | 458.sjeng | 470.lbm
LI Instruction cache misses | 994 | 676 | 1409 | 2774 | 546
L1 Data cache misses | 2044633 | 10225987 | 118032 | 8422662 | 7161902
L2 cache misses | 645445 | 6352827 | 6100 | 8377166 | 7149444
Number of Instructions | 500000000 | 500000000 | 500000001 | 500000000 | 500000000
CPI | 1.089092024 | 1.758002656 | 1.0020432919 | 1.938821832 | 1.800893776

## Slide 12: Configurations
PARAMETERS | VALUES
CPU TIMING | Deriv03CPU(Detailed)
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 2
BLOCK SIZE | 64kB
L1 DATA CACHE SIZE | 128kB
L1 DATA ASSOCIATIVITY | 2
L1 INSTRUCTION CACHE SIZE | 128kB
L1 INSTRUCTION ASSOCIATIVITY | 2

## Slide 13: CPI OF ALL THE BENCHMARKS
 | 401.bzip2 | 429.mcf | 456.hmmer | 458.sjeng | 470.lbm
LI Instruction cache misses | 994 | 676 | 1409 | 2774 | 546
L1 Data cache misses | 2044633 | 10225987 | 118032 | 8422662 | 7161902
L2 cache misses | 645445 | 6352827 | 6100 | 8377166 | 7149444
Number of Instructions | 500000000 | 500000000 | 500000001 | 500000000 | 500000000
CPI | 1.996435322 | 1.78532203 | 1.568432124 | 1.9434392132 | 1.774232932

## Slide 14: PART 3
CPI optimization of each benchmarks

## Slide 15: Script for Creating Different Combinations of Benchmark

## Slide 16: Script for Creating Different Combinations of Benchmark

## Slide 17: Script for Creating Different Combinations of Benchmark

## Slide 18: Design Parameters to Optimize CPI for 401.bzip Benchmark
PARAMETERS | VALUE
CPU TIMING | TIMING
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 1
BLOCK SIZE | 64KB
L1 DATA CACHE SIZE | 64KB
L1 DATA ASSOCIATIVITY | 1
L1 INSTRUCTION CACHE SIZE | 128KB
L1 INSTRUCTION ASSOCIATIVITY | 1
Optimal CPI | 1.56302464

## Slide 19: Optimized CPI of 401.bzip
Chart: 401.bzip2 CPI vs Parameters
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis - CPI

## Slide 20: CPI Analysis
Chart: Effect of L2_Caches on CPI
Chart: Effect of D-Cache and I-Cache on CPI
Chart: Effect of D-Asso on CPI
Chart: Effect of I-Asso on CPI
Chart: Effect of Block Size on CPI

## Slide 21: CPI Analysis
From the line chart analysis, we obtained the following results:
  Greater L2 size results in better CPI.
  Higher the L2 associativity and L1 data associativity, better the CPI.
  Greater the block size, better the CPI.
  Varying L1 data size, L1 instruction size and L1 instruction associativity has no significant impact on CPI.

## Slide 22: Design Parameters to Optimize CPI for 429.mcf Benchmark
PARAMETERS | VALUE
CPU TIMING | TIMING
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 1
BLOCK SIZE | 64KB
L1 DATA CACHE SIZE | 64KB
L1 DATA ASSOCIATIVITY | 1
L1 INSTRUCTION CACHE SIZE | 128KB
L1 INSTRUCTION ASSOCIATIVITY | 1
Optimal CPI | 1.49935404

## Slide 23: Optimized CPI of 429.mcf
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis - CPI
Chart: 429.mcf CPI vs Parameters
1.49935404

## Slide 24: CPI Analysis
Chart: Effect of L2 Cache on CPI
Chart: Effect of D-Asso on CPI
Chart: Effect of I-Asso on CPI
Chart: Effect of D-cache and I-cache on CPI
Chart: Effect of Block size on CPI

## Slide 25: CPI Analysis
From the line chart analysis, we obtained the following results:
  Varying L2 size, L2 associativity, L1 data size and L1 data associativity has little impact on CPI.
  Greater the block size, better the CPI.
  Varying L1 instruction size and L1 instruction associativity has no significant impact on CPI.

## Slide 26: PART 3: Design parameters to Optimize CPI For 470.lbm Benchmark
PARAMETERS | VALUE
CPU TIMING | TIMING
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 1
BLOCK SIZE | 64KB
L1 DATA CACHE SIZE | 128KB
L1 DATA ASSOCIATIVITY | 1
L1 INSTRUCTION CACHE SIZE | 128KB
L1 INSTRUCTION ASSOCIATIVITY | 1
Optimal CPI | 1.9965286

## Slide 27: Optimized CPI of 470.lbm
Chart: 470.lbm CPI vs Parameters
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis - CPI
Optimal CPI = 1.9965286

## Slide 28: CPI Analysis
Chart: Effect of I_Asso on CPI
Chart: Effect of D_Asso on CPI
Chart: Effect of Block Size on CPI
Chart: Effect of D-Cache and I-Cache on CPI
Chart: Effect of L2_Cache on CPI

## Slide 29: CPI Analysis
From the line chart analysis, we obtained the following results:
  Varying L2 size, L2 associativity, L1 data size, L1 data associativity, L1 instruction size and L1 instruction associativity have no significant impact on CPI.
  Greater the Block size, better the CPI.

## Slide 30: Design parameters to Optimize CPI for 456.hmmer Benchmark
PARAMETERS | VALUE
CPU TIMING | TIMING
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 1
BLOCK SIZE | 64KB
L1 DATA CACHE SIZE | 32KB
L1 DATA ASSOCIATIVITY | 1
L1 INSTRUCTION CACHE SIZE | 128KB
L1 INSTRUCTION ASSOCIATIVITY | 1
Optimal CPI | 1.00526852

## Slide 31: Optimized CPI of 456.hmmer
Chart: 456.hmmer CPI vs Parameters
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis - CPI

## Slide 32: CPI Analysis
Chart: Effect of L2_Cache on CPI
Chart: Effect of I-Asso on CPI
Chart: Effect of D-Asso on CPI
Chart: Effect of Block Size on CPI
Chart: Effect of D-Cache and I-Cache on CPI

## Slide 33: CPI Analysis
From the line chart analysis, we obtained the following results:
  Varying L2 size, L2 associativity, L1 instruction size and L1 instruction associativity has no significant impact on CPI.
  Block size and L1 data associativity have moderate impact on CPI.
  Greater the L1 data size, better the CPI.

## Slide 34: Design parameters to Optimize CPI For 458.sjeng Benchmark
PARAMETERS | VALUE
CPU TIMING | TIMING
L2 CACHE SIZE | 1MB
L2 ASSOCIATIVITY | 1
BLOCK SIZE | 64KB
L1 DATA CACHE SIZE | 128KB
L1 DATA ASSOCIATIVITY | 1
L1 INSTRUCTION CACHE SIZE | 64KB
L1 INSTRUCTION ASSOCIATIVITY | 1
Optimal CPI | 1.99383124

## Slide 35: Optimized CPI of 458.sjeng
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis - CPI
Chart: 458 CPI vs Parameters

## Slide 36: CPI Analysis
Chart: Effect of L2_Cache on CPI
Chart: Effect of I-Asso on CPI
Chart: Effect of D-Asso on CPI
Chart: Effect of Block Size on CPI
Chart: Effect of D-Cache and I-Cache on CPI

## Slide 37: CPI Analysis
From the line chart analysis, we obtained the following results:
  Varying L2 size, L2 associativity, L1 data size, L1 data associativity, L1 instruction size and L1 instruction associativity have no significant impact on CPI.
  Greater the Block size, better the CPI.

## Slide 38: Optimal CPI value of each Benchmarks
Benchmarks | Optimal Value
401.bzip2 | 1.56302464
429.mcf | 1.49935404
470.lbm | 1.9965286
456.hmmer | 1.00526852
458.sjeng | 1.99383124

## Slide 39: Part 4 - Cost Function
Parameters | Cost units | Cost per unit
Block Size of 32 bytes | 32 | 32
Block Size of 64 bytes | 64 | 64
L1 Instruction Data Caches of 32 KB | 64 | 64
L1 Instruction Data Caches of 64 KB | 64 | 64
L1 Instruction Data Caches of 128 KB | 128 | 128
L2 Cache of 1MB | 1024 | 1024
1-way associative Cache | 1 | 1
2-way associative Cache | 2 | 2
4-way associative Cache | 4 | 4
8-way associative Cache | 8 | 8
L1:L2 cost ratio | 4 | 4

## Slide 40: Cost Formula
Cost = Block_sizecost+L1:L2 cost ratio x {(L1_I_Cachecost×Associativitycost)+ (L1_D_Cachecost×Associativitycost)} + (L2_cachecost × L2_associativitycost)
FUNCTION | FORMULA
Cost Evaluation Function | Total Cost * CPI
Total Cost | L2 Cost + Block Size Cost + L1 D Cost + L1 I Cost
L2 Cost | L2 Size Cost * L2 Associativity Cost
L1 Data Cost | L1 D Size Cost * L1 D Associativity Cost
L1 Instruction Cost | L1 I Size Cost * L1 I Associativity Cost

## Slide 41: PART 5
Optimize caches for Performance/Cost

## Slide 42: Part 5: Optmized CPI * Cost – 401. bzip2
Chart: 401.bzip2 Cost*CPI vs Parameters
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis – Cost*CPI

## Slide 43: Part 5: Optmized CPI * Cost – 429.mcf
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis – Cost*CPI
Chart: 429 Cost*CPI vs Parameters
Optimal Cost*CPI

## Slide 44: Part 5: Optmized CPI * Cost – 470.lbm
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis – Cost*CPI
Chart: 470.lbm Cost*CPI vs Parameters
Optimal Cost*CPI

## Slide 45: Part 5: Optmized CPI * Cost – 456.hmmer
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis – Cost*CPI
Chart: 456.hmmer Cost*CPI vs Parameters

## Slide 46: Part 5: Optmized CPI * Cost – 458.sjeng
X axis – Dsize_Isize_Dasso_Iasso_Blocksize
Y axis – Cost*CPI
Chart: 458.sjeng Cost*CPI vs Parameters
Optimal Cost*CPI

## Slide 47: Optimized Cost*CPI for each Benchmark
PARAMETERS | 401.bzip2 | 429.mcf | 456.hmmer | 458.sjeng | 470.lbm
CPU Type | Timing | Timing | Timing | Timing | Timing
L2 Size | 1MB | 1MB | 1MB | 1MB | 1MB
L2 Associativity | 1 | 1 | 1 | 1 | 1
Block Size | 64KB | 64KB | 32KB | 64KB | 32KB
L1 Data Size | 32KB | 32KB | 32KB | 32KB | 32KB
L1 Data Associativity | 1 | 1 | 1 | 1 | 1
L1 Instruction Size | 32KB | 32KB | 32KB | 32KB | 32KB
L1 Instruction Associativity | 1 | 1 | 1 | 1 | 1
Optimal Cost*CPI | 2032.68354 | 1887.552684 | 1324.275124 | 2193.539604 | 2624.95545

## Slide 48: Conclusion
We have observed that the Block size, Cache size and associativity are the major parameters in optimizing both CPI and Cost of each Benchmarks.
Size plays the major factor in defining cost function.
The optimized cache configuration for each benchmarks was calculated by the product of CPI and Cost.
The least value of the cost evaluation function indicates the optimum cache configuration.

## Slide 49
THANK YOU